## Slide 1: Unit 7 Microbiology
Chapter 37
Introduction to Microbiology

## Slide 2: Objectives
List and select the appropriate media that provide a growth environment for specified bacteria and describe the growth curve.
Aseptically collect a bacterial sample, inoculate a medium and culture growth, transfer colony samples to a slide for fixing, stain the sample (using Gram’s, Acid-Fast, or Giemsa stain), and evaluate.
Identify various selected bacterial species and describe the diseases they may cause.
Identify common animal pathogens using commercially available media and reagents, perform common biochemical tests, and perform one of the antimicrobial susceptibility tests studied.

## Slide 3: Microbiology Basics
A basic understanding of the characteristics of bacteria, fungi, and viruses will aid the veterinary technician in collection, handling, and evaluation of samples.
Identification of bacterial, fungal, and viral pathogens is the primary purpose of microbiologic examinations.

## Slide 4: Bacterial
Prokaryotic—no nuclear membrane
  Most cellular organelles are absent, except cell walls, plasma membranes, and ribosomes.
  Some may contain capsules and flagella and can develop endospores.
Have requirements for temperature, pH, oxygen tension, and nutrition
  Considered when collecting and preparing samples
  Used to help identify samples

## Slide 5: Oxygen Requirements
Obligate aerobes—require O2 to survive
Obligate anaerobes—growth inhibited or killed in the presence of O2
Facultative anaerobes—can survive in O2 but growth is limited
Microaerophilic—prefer reduced O2 tension
Capnophilic—require high levels of carbon dioxide

## Slide 6: Other Requirements
pH—most live in the range of 6.5 to 7.5
Temperature
  Mesophiles—almost all pathogenic bacteria in animals grow best at 20° C to 40° C
  Psychrophiles—lower temperatures
  Thermophiles—higher temperatures

## Slide 7: Morphology
Classified by shape and arrangement

## Slide 8: Spores
Some genera of bacteria have endospores
  Resistant to heat, desiccation, chemicals, and radiation
  Location in cell helps classify

## Slide 9: ????
Name the 3 of the bacteria arrangements.

## Slide 10: Equipment and Supplies

## Slide 11: In-House Microbiology Laboratory
Ideally in a separate room away from the main traffic areas
Should have
  Adequate lighting and ventilation
  A washable floor
  Limited traffic
  At least two work areas
    Processing and culture work
  Smooth surfaces—easily disinfected
  Electrical outlets
  Ample storage
  Easy access to incubator and refrigerator

## Slide 12: Laboratory Safety
Potentially pathogenic and/or zoonotic
Aseptic technique
Personal protective equipment
  Long sleeves, knee-length white laboratory coat or clean surgical scrubs
  Gloves
  Face masks
  Eye protection
Wash hands
Autoclave or dispose of properly
Treat spilled cultures with disinfectant—20 minutes
No eating, drinking, handling contact lenses, or cosmetics
Hair pulled back
Report accidents promptly

## Slide 13: Equipment and Supplies
A good-quality incubator capable of maintaining constant temperature and humidity
Collection and preparation supplies
  Sterile cotton-tipped swabs
  Dull scalpel blades
  3- to 20-mL syringes and 21- to 25-g needles
  Sterile endotracheal tube or jugular or urinary catheter
  Collection tubes and preservatives
  Rayon swabs in transport media
  High-quality glass slides and coverslips

## Slide 14: Equipment and Supplies Cont.
Inoculating loops or wires—reusable metal or disposable plastic
Bunsen burner or alcohol lamp
Candle jar
Variety of culture media
Antibiotic discs and dispensers
Gram stains and other stains
Scissors, forceps
Discard jar—disinfectant
Wooden tongue depressors
Racks for tubes
Refrigerator—cold packs and polystyrene shipping containers

## Slide 15: Culture Media
Any material, solid or liquid, that can support the growth of microorganisms.
Agar is dried extract of sea algae.
Gelatin is a protein obtained from animal tissues.
Store refrigerated at 5° C to 10°C
  Away from inside wall to avoid freezing

## Slide 16: Types of Media
Transport
  Keep microbes alive but do not encourage growth
General purpose
  Enriched
    Meet requirement of fastidious pathogens
  Selective
    Contain antibacterial substances
  Differential
    Allow bacteria to differentiate into groups by biochemical reactions
  Some medias contain more than one type.

## Slide 17: Blood Agar
Enrichment and a differential media
  Trypticase soy agar with sheep blood—most common
  Four distinct types of hemolysis can be detected.
    Alpha—partial hemolysis creates a band of greenish or slimy discoloration around the colony.
    Beta—complete hemolysis creates a clear zone around the colony.
    Gamma—hemolysis that produces no change in the appearance of the medium.
    Delta— double zone hemolysis.

## Slide 18: Hemolysis

## Slide 19: MacConkey Agar and Eosin-Methylene Blue Agar
Selective and differential media
MacConkey contains:
  Crystal violet (suppress growth of Gr + bacteria)
  Bile salts—selective for lactose-fermenting Enterobacteriaceae
EMB—performs the same function as MacConkey agar
    may also be used to identify lactose-fermenting organisms.

## Slide 20: Chromogenic Agar
Both selective and differential media.
Provide sufficient information to definitively identify some bacterial species.
Examples of chromogenic agar include several types designed to identify certain resistant bacteria based on their color and colony appearance on the specific chromogenic agar.

## Slide 21: Thioglycollate Broth
Liquid medium used to culture anaerobic bacteria to determine O2 tolerance of microbes.
Obligate aerobes will only grow in the top layer.
Obligate anaerobes grow in the lower portion.
Facultative—throughout the medium but best in middle of tube.

## Slide 22: Sulfide-Indole Motility Tubes
Inoculated with a straight stab to approximately 1 inch deep
  Draw wire out same line as entry
Hydrogen sulfide production indicated by blackening of the medium
Used to differentiate members of Enterobacteria

## Slide 23: Mueller-Hinton
General purpose
  Performance of the agar diffusion antimicrobial sensitivity test.
  Chemical composition does not interfere with diffusion of antimicrobials through agar.

## Slide 24: Combination and Modular Culture Media
Most commonly used modular media includes the Bullseye system, Uri-Cult, and Spectrum plates.
Bullseye culture media. The center section contains Mueller- Hinton media for performing the antibiotic susceptibility test.
Spectrum CS plate showing gram-positive, gram-negative, Staphylococcus select, and blood agar areas.

## Slide 25: Enterotubes
The enterotube is a multitest system that contains eight different agar preparations.

## Slide 26: ????
What are the 4 types of hemolysis?

## Slide 27: Sample Collection and Handling

## Slide 28
What are 3 common agar plates?

## Slide 29: Sample Collection
Samples collected by various methods
  Aspiration
  Swabbing
  Imprints
Specific sampling technique used depends on type of lesion and location.
Aseptic technique critical

## Slide 30: Aspiration
Hollow organs
  Bladder
External lesions
  Pustules

## Slide 31: Swabs
Sterile
Samples that are to be processed immediately.
Least suitable method
  Contamination risk is high.
  Cotton can inhibit microbial growth.
  Oxygen trapped in fibers—anaerobes
If delays expected
  Culturette (transport media)

## Slide 32: Specimens
Must contain the organism causing the problem.
Normal flora and contaminants may complicate collection and results.
Best to use techniques that would be normally sterile and aseptic techniques.
  Urine—cystocentesis
  Intact pustules
  Ears and fecal samples—not optimal

## Slide 33: Guidelines for Proper Collection
Complete history and sufficient clinical data to help select procedures to best isolate organisms that may be present.
Data labeled and complete information supplied
  Owner’s name
  Clinic name
  Address and phone number
  Species, name, age, gender, number of animals affected or dead
  Duration of the problem
  Major signs observed
  Tentative diagnosis
  Organism suspected
  Any treatment given
  Type of laboratory investigation required

## Slide 34: Guidelines for Proper Collection
Collect specimen aseptically
Collect as soon as possible after onset
Multiple specimens must be kept separate to avoid cross-contamination.
Container labeled
  Especially zoonotic-suspected organism
  Specimens submitted in sealed, leak-proof, unbreakable container

## Slide 35: ????
What is aseptic technique? Should we use it while colleting samples/culturing?

## Slide 36: Staining Specimens

## Slide 37: Stains
A variety of stains available
Most common
  Gram stain
  Ziehl-Neelsen (acid-fast) stain
Stain before culturing
  Rapid identification
  Determine appropriate medium
  Determine appropriate antibacterials

## Slide 38: Stains Cont.
Simple stains
  Crystal violet and methylene blue
    Typically used for yeasts
  Lactophenol cotton blue
    Confirms identity of fungal organisms
Many stains available but most are performed only in large reference or research laboratories.

## Slide 39: Gram Stain
Used to categorize bacteria
  Gram-positive or gram-negative
    Based on cell wall structure
Requires four steps
  Primary stain, a mordant, a decolorizer, and a counterstain
    Mordant—fixes dyes to the structures (cell wall)
    Primary stain usually crystal violet
    Mordant—Gram’s iodine solution
    Decolorizer—95% ethanol or acetone
    Counterstain—basic fuchsin or safranin

## Slide 40: Why do bacteria stain differently?
Gram-positive and Gram-negative bacteria stain differently because of fundamental differences in the structure of their cell walls.
  Gram-positive cell wall appears as a broad, dense wall 20-80 nm thick and consisting of numerous interconnecting layers of peptidoglycan
  Gram-negative cell wall, on the other hand, contains only 2-3 layers of peptidoglycan and is surrounded by an outer membrane composed of phospholipids, lipopolysaccharide, lipoprotein, and proteins

## Slide 41: Gram Stain Procedure
Video
Video

## Slide 42: Gram Stain Interpretation
Gram-positive
  Bacteria that retain the violet-iodine complex stain purple.
Typical staining pattern of gram-positive Actinomyces bacteria

## Slide 43: Gram Stain Interpretation
Gram-negative
  Loose the crystal-violet or purple color and stain red
Typical staining pattern of gram-negative Yersinia bacteria

## Slide 44: Potassium Hydroxide Test (KOH)
Determines the true Gram status
Gram variable reaction
  May be because of excessive decolorization, an overly thick sample, excessive heat fixing, old cultures, or poor-quality stain

## Slide 45: ????
How many stains are in a grams stain kit?

## Slide 46: Potassium Hydroxide Test
A loopful (or two) of 3% KOH solution placed on slide
A generous quantity of surface growth from culture transferred to the KOH
Stir specimen (30 seconds to 2 minutes)
  Then gently lift the loop
    Gram-negative develop a mucoid appearance and produce a sticky strand
    Gram-positive—mixture remains homogeneous, no strand

## Slide 47: Oxidase Test
Supplies
  Chemical-1% tetramethyl-p-phenylendiamine
  Filter paper
  Sampler
  Sterile loop
Procedures
  Oxidase Test

## Slide 48: Culture Techniques

## Slide 49: Culturing Specimens
A systematic approach is needed to identify pathogenic bacteria.
Develop flowcharts for use in the clinic for the most commonly seen bacteria.
  Include tests to differentiate those bacteria

## Slide 50: Flowchart
Examples of flow charts that are used for the differentiation of bacteria.

## Slide 51: Presumptive Identification
Staining and culturing
  Veterinarian may start treatment based on results.
Plate suspected pathogens on primary medium
  Blood agar or MacConkey agar
  Incubate for 18 to 24 hours—examine for growth
  Follow flow chart for further identification
Definitive identification
  Requires additional biochemical testing

## Slide 52: Presumptive Identification
Blood agar
  Grows both gram-positive and gram-negative
MacConkey agar
  Gram-positive organisms do not grow.
  May inhibit growth of potentially pathogenic bacteria

## Slide 53: Inoculation of Culture Media
Aseptic technique at all times
  Sear surface of cadaver or excised organs
  Culture plates kept closed except when removing specimens.
  Flame wire—start at near end first and work toward distal end.
    Could cause splattering of bacteria—aerosolized

## Slide 54: Quadrant Streaking Method
Designed to aid in isolation of pure bacterial cultures
The quadrant streak method for the isolation of bacteria

## Slide 55: Inoculations of Tube Media
Enough bacteria should be on the wire to inoculate the surface even after stabbing the butt.
Slant surface inoculated in an “S” shape.
Tube cap on loosely.

## Slide 56: Inoculations of Cultures
For most pathogens, incubate at 37º C
Some fish, skin pathogens, and environmental organisms, incubate lower than 37º C
Incubation time depends on the generation time of the species and type of medium.
  Most are 48 hours with examination at 18 to 24 hours.
  Incubate plates inverted to prevent condensation on the surface of the plate.

## Slide 57: Candle Jar
For pathogens that require carbon dioxide for growth.
Place plates in a large jar
Place a lit candle on top of the plates and seal jar
The candle dies, leaving a decreased amount of oxygen and an increase in CO2 in the jar
  Not anaerobic condition
Examine plates for 18 to 24 hours; if no growth, reincubate in jar for another 18 to 24 hours
Large laboratories have incubators that control temperature, CO2, O2, and humidity.

## Slide 58: Colony Characteristics
Size
Pigment
Density
Elevation
Form
Texture
Odor
Any hemolysis
Bacterial colonies may be described on the basis of their form, elevation, and margins.

## Slide 59: ????
Why should you describe a bacteria colony?

## Slide 60: Antimicrobial Sensitivity Testing

## Slide 61: Antibiotic Resistance
One of the world’s most pressing public and animal health problems.
Occurs when a microbe changes or mutates in some way that reduces or eliminates the effectiveness of drugs, chemicals, or other agents designed to cure or prevent infections.
Exposure to antibiotics therefore provides selective pressure, which makes the surviving bacteria more likely to be resistant.
When antibiotics are used kill or inhibit the growth of susceptible bacteria, sometimes one of the bacteria survives
  That one bacterium can then multiply and replace all the bacteria that were killed off.

## Slide 62: Antibiotic Resistance
Resistance can also develop through mutation of their genetic material or by acquiring pieces of DNA that code for the resistance properties from other bacteria.
Some bacteria develop the ability to neutralize the antibiotic before it can do harm, others can rapidly pump the antibiotic out, and still others can change the antibiotic attack site so that it cannot affect the function of the bacteria.

## Slide 63: Antimicrobial Sensitivity
Performed to determine the susceptibility or resistance to specific antimicrobial drugs.
Helps veterinarian choose the most appropriate antimicrobial for the patient.

## Slide 64: Agar Diffusion Method
Most commonly preferred method
  Uses paper discs impregnated with antimicrobials
  Quantitative and requires the measurement of inhibitory zone sizes
    Gives an estimate of susceptibility
  Concentrations on discs correlate with therapeutic levels of the drugs in tested animals

## Slide 65: Antimicrobial Discs (1 of 2)
Kept in the refrigerator when not used .
Outdated discs should not be used.
Potency of discs monitored with control organisms.
A disc dispenser for placement obtained from the manufacturer of the discs.
Caliper for measuring (Or clear ruler).

## Slide 66: Indirect Sensitivity Testing
Requires that colony samples be taken from a culture plate and subcultured in broth media.
  Incubate to achieve turbidity to match a standardized 0.5 McFarland suspension.
The broth suspension is then applied to Mueller-Hinton media with a swab or loop to cover the plate evenly.
McFarland standard suspensions

## Slide 67: Indirect Versus Direct
Indirect testing is more precise than direct testing, but results are not available as quickly.

## Slide 68: Direct Testing Method
Application of undiluted samples (urine etc.) directly to a Mueller-Hinton plate
  Not as precise
  Reasonable results if only one organism is present.
  Interpret with caution if multiple organisms are present.

## Slide 69: Disc Placement
Dispenser or sterile forceps
  Flamed and cooled between each use
10 to 15 mm apart
  Avoid overlapping of ZOI
Place disc into the agar with a sterile swab
Incubate, inverted and aerobic at 37º C, within 15 minutes of disc placement
Stacks of four or fewer
  If taller, the middle plates take longer to get to temperature.

## Slide 70: Zone of Inhibition
Measurement is compared to a chart of ZOI to determine the relative resistance of the bacterium to the antimicrobial.
The zone sizes are divided into two major categories: resistant or susceptible to the particular antimicrobial agent.
  The susceptible category is subdivided into intermediate susceptibility and susceptible.

## Slide 71: Reading of ZOI
Plates read after a constant time period
  Usually 18 to 24 hours
  Prolonged incubation may alter the size of ZOI
Zones read from the bottom of the plate using a caliper, transparent ruler, or template
Measured to the nearest millimeter
The use of calipers to measure the zone of inhibition

## Slide 72: Minimum Inhibitory Concentration
Minimum inhibitory concentration (MIC) of an antimicrobial is the lowest concentration of a specific antimicrobial that can inhibit the growth of a given bacteria.
Choice of a specific concentration of antimicrobial is based on the MIC, the site of infection, and the breakpoint of the antimicrobial.
AB Sensitively

## Slide 73: ????
What is a ZOI?

## Slide 74: Additional Testing

## Slide 75: Additional Testing
Motility
Catalase test
Coagulase test
Oxidase activity
Acid production from glucose
California mastitis test
Immunologic examination

## Slide 76: Motility
Wet prep
  Young broth culture
  A loopful of culture placed on slide under coverslip
  Examined with high dry objective
    Look for motile—cells moving back and forth among other cells
  Observe quickly—evaporation
  Brownian movement—not true motility
    Shifting of cells with little movement related to other cells

## Slide 77: Catalase Test (1 of 2)
Performed on gram-positive cocci and small gram-positive bacilli
Tests for the enzyme catalase
  Acts on hydrogen peroxide to produce water and oxygen
  Small amount of a colony from a blood agar plate is placed on a microscope slide and a drop of catalase reagent (3% H2O2) is added.
  Gas bubbles—catalase positive (Staph)
  No bubbles—negative (Strep)
A positive catalase test is indicated by the production of bubbles after hydrogen peroxide has been added to a sample on a slide.

## Slide 78: Catalase Test (2 of 2)
False-positives
  If blood agar is included in sample
  If a mixed colony

## Slide 79: Bacteria of Veterinary Importance

## Slide 80: Spirochete

## Slide 81: Spirochetes
*Leptospira spp- *Zoonotic*
  “Leptospirosis” “Lepto”
  Renal and hepatic damage, fever, depression, anorexia and jaundice.
    Shed in urine of infected animals
  Common in dogs, cows, horses, pigs
  Reservoir: rodents raccoon and skunks
  Vaccination available (DHLPP)
  Causes abortions in Equine, Bovine, Ovine and HUMANS!!
    DX- serology

## Slide 82: Spirochetes
*Borellia burgdorferi
“Lyme DZ”
Transmitted by
  Ixodes tick
Clinical signs- intermittent shifting, lameness, mild fever, depression, fatigue, bulls eye lesions, vague flu-like symptoms, cardiac abnormalities, anorexia stiff and painful.
      Progressive DZ
        Arthritis
        Laminitis(Inflammation of equine hoof)
        Neurological signs
DZ- serology or ELISA

## Slide 83: Spiral and curved bacteria
*Campylobactor
  Normal flora in dogs
  Looks like flying seagulls(curved rods, darting motility) on fecal smear
  Causes “wet tail” in hamsters
  Winter dysentery in cattle and sheep
  Enteritis in many other animals and humans

## Slide 84: Bacillus

## Slide 85: Gram Negative Rods Facultative
*Escherichia coli (E.coli)
Opportunistic E. coli
  Normal flora
  Mastitis in dairy cows
  Cystitis in humans and animals
Enteropathogenic E.coli
  Gastroenteritis in newborns, calf scours (diarrhea)
    Invasive Enteropathic E. coli- tissue invasion, bloody diarrhea HIGHLY FATAL
    Enterotoxin producing e. coli- binds to intestinal epithelium cells, disrupts cell membranes- cells loose water, electrolytes and death due to dehydration and metabolic acidosis

## Slide 86: Gram Negative Rods Facultative
Klebsiella pneumoniae
- encapsulated bacteria mucoid colony
  Pneumonia
  Systemic infections
  Antimicrobial resistance
  Normal flora of GI and commonly found in Feces

## Slide 87: Gram Negative Rods Facultative
Proteus – highly motile bacteria, swarming colony morphology and STINKY!!
  Normal flora of intestines
  Nosocomial infections- long term care facilities

## Slide 88: Gram Negative Rods Facultative
Salmonella typhi
  Fecal-oral transmission
  “Typhoid fever”
  Reptiles and turtles carry as normal flora!!
Sources
  Reptiles!
  Raw or undercooked meats/eggs
  Dairy products
  Veggies

## Slide 89: Gram Negative Rods Facultative
Shigella- similar to salmonella
  “Shigellosis”
    Diarrhea
    Fever
    Stomach cramps

## Slide 90: Gram Negative Rods Facultative
*Yersinia pestis
  BLACK PLAGUE!!!!!
  Reservoir host- rodents (prairie dogs)
  Vector fleas
  Endemic to a geographical location
  3 types in Humans
    Bubonic-most common
    Septicemic- High fever
    Pneumonic- lungs (aerosolized)

## Slide 91: Gram Negative Rods Facultative *Pasturella Spp.
P. hemolytica-
  Cattle- “Shipping Fever” (pneumonia)
  Bacteria + IBR virus + stress (shipping)
P. multocida-
  Rabbits- “Snuffles” a resp. infection
  Settles in the conjunctiva ocular discharge otitis & balance disturbances abscesses cottage cheese pus
  Birds- “Avian Cholera”, resp. infection, 60% fatal
  Dogs/Cats- bite wound abscesses
  People- cat bite transmission, normal flora in saliva

## Slide 92: Gram Negative Rods Facultative
Other GNR
  Serratia
    capable of thriving in diverse environments, including water, soil, and the digestive tracts of various animals
  Enterobacter
    bacteremia, lower respiratory tract infections, skin and soft-tissue infections, urinary tract infections (UTIs), endocarditis, intra-abdominal infections, septic arthritis, osteomyelitis, CNS infections, and ophthalmic infections.
  Citrobacter
    UTI, wound infection and mastitis

## Slide 93: Gram Negative Rods Aerobic
Pseudomonas aeruginosa
  Antibiotic resistant
  Strong odor-Fruity smell
  Blue/green/ yellow/green pigment
  Nosocomial infections
  Opportunistic pathogen
    Burns
    Wounds
    Surgical incision

## Slide 94: Gram Negative Rods Aerobic
*Francisella tularemia
  Rabbit fever
  Reservoir- rabbits, rodents
  Vector –ticks
    Ingestion of tainted rabbit meat
    Dx with serology

## Slide 95: Gram Negative Rods Aerobic
*Brucella
  Can remain viable up to 4 months in urine, milk, soil, placenta or aborted fetus
    Brucella canis
      No immunization
      Common in stay dogs
        Abortions
        Mastitis
        Infertility/conception failures

## Slide 96: Gram Negative Rods Aerobic
Brucella
    Brucella abortus
      Cattle, elk, moose
      No Tx
      Abortion
      Mastitis
      Infertility/conception failures
        Known as Bangs Dz in cattle
        Indulant Fever in humans

## Slide 97: Gram Negative Rods Aerobic
    Brucella melitensis
      Cattle, sheep, goats, camels, llamas
      Highest pathogenicity
    Brucella ovis
      Sheep, mostly rams
  Brucella suis
      Swine
      No immunization
      High pathogenicity

## Slide 98: Gram Negative Rod Aerobic
*Bordetella bronchiseptica
  Pili infection via Inhalation
  Highly contagious due to aerosol transmission
  Immunization available in dogs and cats
    “Kennel cough” cough, cough, gag
      Dogs, cats, lab animals and wild life
  Atrophic rhinitis
    In young pigs

## Slide 99: Gram Negative Rod Anaerobic rods
Fusobacterium
  Thrush in Horses
    Infection of the hoof , specifically the frog
      Wet, muddy, unsanitary horse stalls, lack of husbandry
      Pick the hoof!

## Slide 100: Gram Negative Rod Anaerobic
Bacteroides
  Normal Flora in mm
  Opportunistic pathogen
    Present in severe gingivitis and periodontal DZ
    Foot rot in Large animals

## Slide 101: Gram negative rod Aerobic
*Bartonella
  Cat scratch DZ
  90% of cases are from playful kittens
  Systemic infection in immunocompromised
  Self – limiting
  Vector-Fleas

## Slide 102: Gram Positive Rods Aerobic
Bacillus anthracis
  “Anthrax”
  Cattle and sheep most susceptible
  Sudden death
  Fatal in 24 hours
Spores in the soil are ingested
  CNS- convulsions, coma
CVS- blood vessel damage, tissue necrosis, shock from fluid loss.

## Slide 103: Gram Positive Rod Anerobic
*Clostridium botulinum
  Botulism
    Spore former
    Motile
    Immunization available for all types of Clostridium
Transmission
  ingestion of NEUROTOXIN
Antitoxin available for people and horses
Bo-Tox skeletal muscle paralysis

## Slide 104: Gram Positive Rod Anerobic
Clostridium botulinum
    Limberneck- in waterfowl, shore birds and scavengers
      Water fowl are very susceptible (eating from the bottom of ponds)
    Shaker foal- Young horses
      Toxin acts at neuromuscular junction, prevents the release of Acetylcholine, results in muscle weakness and paralysis

## Slide 105: Gram Positive Rod Obligate anerobe
*Clostridium tetni
  Tetanus
  Ubiquitous (common in soil)
  Motile
  Spore forming
Transmission
  deep puncture wounds endotoxin release CNS inhibitory neurons no muscle relaxation.
“Tetnospasms” strong enough to break bones, “Lockjaw” (humans)

## Slide 106: Gram Positive Rod Obligate anerobe
Clostridium perfringies
  Ingestion of spores
  Food poisoning
  Hemorrhagic enteritis

## Slide 107: Gram Positive Rods Facultative anaerobe
Corynebacterium pseudotuberculosis
  Lymphadenitis in sheep and goats, thick cheesy pus
  Ulcerative lymphadenitis in horses and mules (“Dryland Distemper”)

## Slide 108: Gram Positive Rods Facultative aerobe
Rhodococcus equi
  Intracellular
  Bronchopneumonia in foals, “Abscessing pneumonia”
  Symptoms- dyspnea, loud moist rale sounds, anorexia, fever

## Slide 109: Gram Positive Rods Faculatative Anerobe
Listeria monocytogenes
  Has flagella
  Ubiquitous- soil, pond water, meat, milk, feces
  “Circling DX”, unilateral ataxia

## Slide 110: Gram negative pleomorphic/Aerobic (ability to change shape/size)
*Mycobacterium
  Tuberculosis-DZ
  Rod shaped, unusual cell wall,
  Antibiotic resistant
  Survive phagocytosis
  Inverse Zoonosis
    Leading bacteria killer in the world
  Tuberculosis(2 types)
    Inhalation-pulmonary TB
      Lesions in the lungs
    Ingestion- ailmentary TB
      Lesion in intestines, liver, spleen
      Common in people before pasteurized of milk

## Slide 111: Gram negative pleomorphic (ability to change shape/size)
  Mycobacterium bovis
    Can also cause TB in humans
    Affect Cattle, Elk Bison and Deer
    Inspectors test more than one million animals a year for TB

## Slide 112: Gram negative pleomorphic Intracellular/Rickettsia
Ehrlichia canis
  Lives in WBCs
  Transmitted by ticks
  Most common in southern state
  Potomac fever- in Equines ( Neorickettsia risticii)
  Immunization available

## Slide 113: Gram negative Pleomorphic Intracellular/Rickettsia
Rickettsia rickettsii (Rocky Mountain spotted fever)
  Dermacentor variabilis (the American dog tick)
  D andersoni (the Rocky Mountain wood tick)
    Rash usually (90% of cases) appears 2-3 days later.
    fever (up to 105°F [40.5°C])
    anorexia
    Lymphadenopathy
    Polyarthritis
    coughing or dyspnea
    abdominal pain, vomiting and diarrhea
    Neurologic manifestations such as altered mental states, vestibular dysfunction

## Slide 114: Gram negative pleomorphic Intracellular/Rickettsia
Anaplasma
  Lives on RBC
  Most common tick born Dz in cattle
  Possible transmission by blood contaminated instruments

## Slide 115: Gram negative pleomorphic
Chlamydia psittaci
  Psittacosis, Parrot Fever or chlamydiosis.
  In birds, C. psittaci may manifest itself as an upper respiratory infection with nasal, and or ocular discharge, diarrhea, or a combination of all three.
  Birds may become carriers and shed the organism.
  A major concern with C. psittaci is the zoonotic potential of the organism.
  C. psittaci is also one of the major causes of infectious abortion in sheep and cattle.

## Slide 116: Mycoplasma haemofelis
Formally Hemobartonella felis
Feline Infectious Anemia
Gram negative pleomorphic

## Slide 117: COCCI

## Slide 118: Catalase Test
Differentiates between:
  Staphylococcus – Positive Catalase
  Streptococcus- Negative Catalase
Reagent is 3% hydrogen peroxide
catalase test

## Slide 119: Gram Positive Cocci (GPC)
*Streptococcus (catalase negative)
  Equi
    Highly infectious
    Equine strangles
  Canis
    UTI infections(cystitis)
  Agalactiae
    Bovine mastitis
  Suis
    Meningitis
    Septicemia
    Pneumonia
    arthritis

## Slide 120: Gram Positive Cocci
Staphylococcus(catalase positive)
  LARGE genus
  Clusters
  Facultative anaerobes and aerobes
  Resistant to drying, disinfectants & Antibiotics
  Normal flora species
  Pathogenic species
  Nosocomial infection
  Exhibits hemolysis- β, alpha and gamma

## Slide 121: Gram Positive Cocci Beta Hemolytic Strep.
*Staphylococcus aureus- beta hemolytic
  Bovine mastitis
  Skin infections/nosocomial infections
  Otitis
  Keratoconjuntivitis=??
  MRSA
Staph intermedius-beta hemolytic
  Most common in dogs
  Otitis
  Mastitis
Staph. hyicus
  Greasy pig Dz
Staph. epidermidis
  Normal flora on skin

## Slide 123: Gram Positive Cocci Hemolytic Strep.
Alpha-
  S. pneumoniae
  S. suis, S. bovis, S. equinus
Gamma-
  S. faecalis (a.k.a. Enterococcus faecalis)- normal flora, rarely a pathogen
  S. uberis- bovine mastitis

## Slide 124: ????
What Species is likely to carry the respiratory Dz Psittacosis?
A Dog
B Bird
C Primate
D Rats

## Slide 125: ????
Is psittacosis zoonotic Dz?

## Slide 126: ???
What sample is the most likely way to contract Leptospirosis?

## Slide 127: ???
Mosquitos are vectors for all of the following except:
  A. Lyme Dz
  B. Canine Heart Worm
  C. Malaria
  D. West Nile Virus

## Slide 128: ???
What is the common name for Borrelia burgdorferi?

## Slide 129: ???
What is the common name for Yersina pestis? What is the vector?

## Slide 130: Objectives
List and select the appropriate media that provide a growth environment for specified bacteria and describe the growth curve.
Aseptically collect a bacterial sample, inoculate a medium and culture growth, transfer colony samples to a slide for fixing, stain the sample (using Gram’s, Acid-Fast, or Giemsa stain), and evaluate.
Identify various selected bacterial species and describe the diseases they may cause.
Identify common animal pathogens using commercially available media and reagents, perform common biochemical tests, and perform one of the antimicrobial susceptibility tests studied.

## Slide 131: The end